## Slide 1: New Campus Network Design GROUP 26
Group Members:
  Law Rou Rou
  Lee Xing Le
  Liew Jieh Cheng
  Tee Yu Chen
  Yen Ming Wey

## Slide 3: Design Overview
Objectives
  Efficient Traffic Management
  Enhanced Security
  Scalability
  Cost-effective
Features implemented
  VLAN segmentation
  Router-on-stick configuration

## Slide 4: VLAN segmentation
VLAN ID | Department | Network Address | Subnet Mask
1 | Finance | 172.19.219.0 | 255.255.255.0
2 | Registry | 172.19.220.0 | 255.255.255.0
3 | HR | 172.19.221.0 | 255.255.255.0
4 | IT | 172.19.222.0 | 255.255.255.0
5 | Servers | 172.19.198.0 | 255.255.255.0
Network is logically separated into 5 VLANs (/24)

## Slide 5: Router-on-stick Configuration
Trunk Switch
VLAN 1
VLAN 2
VLAN 3
VLAN 4
Trunk Port

## Slide 6: Benefits of Implemented Features
VLAN segmentation
Enhanced Security
Isolating departments into separate VLANs
Increase Performance
Smaller broadcast domains reduce unnecessary traffic
Flexibility and scalability
Adding new departments or devices becomes easier
Router-on-stick Configuration
Inter-VLAN Routing
Enables communication between VLANs
Cost-Effectiveness
Uses a single router interface for multiple VLANs

## Slide 7: Router
The GigabitEthernet0/0 interface is connected to the LAN,
while GigabitEthernet0/1 connects to the ISP.
GigabitEthernet0/0.1 for the Finance department: 172.19.219.1
GigabitEthernet0/0.2 for the Registry department: 172.19.220.1
GigabitEthernet0/0.3 for the HR department: 172.19.221.1
GigabitEthernet0/0.4 for the IT department: 172.19.222.1
GigabitEthernet0/1
to ISP
GigabitEthernet0/0
To LAN

## Slide 8: Purpose
Efficient and Centralized Network Architecture
Precise Traffic Control and Routing
Optimized Network Performance and Bandwidth Utilization
GigabitEthernet0/1
to ISP
GigabitEthernet0/0
To LAN

## Slide 9: Purpose-Scalability
Utilizing Sub-Interfaces Instead of Physical Interfaces
Virtual Segmentation for Easy VLAN Expansion
GigabitEthernet0/1
to ISP
GigabitEthernet0/0
To LAN

## Slide 10: Sub-interface Configuration
Diagram: Configuration for finance department

## Slide 11: Routing Configuration
Static Routing between Campus Router and ISP Network
Efficient Data Transfer between Networks

## Slide 12: Inter-VLAN Routing
Successful Testing of Inter-VLAN Communication
Departments with Different Default Gateways Connected Seamlessly
Tracert from one department to another

## Slide 13: Access switch and VLAN
Each department has own access switch
Connect workstations and other devices within the VLAN

## Slide 14: Access Switch
Unique ip address to each department
Finance department – 172.19.219.2 (VLAN 1)
Registry department – 172.19.220.2 (VLAN 2)
HR department – 172.19.221.2 (VLAN 3)
IT department – 172.19.222.2 (VLAN 4)
Allow efficient communication within each department’s network

## Slide 15: Access switch configuration
Using “switchport mode access” and “switch port access vlan1” command
Enable switch into access mode
Specifying appropriate VLAN to each department access switch port
Isolate traffic between departments

## Slide 16: Benefits of access switch and VLAN setup
Enable secure communication within each department
Ensure the data is contained within its designated VLAN

## Slide 17: Switch
Departments | Interface | IP Address
Finance | F0/1 | 172.19.219.3
Registry | F0/2 | 172.19.220.3
HR | F0/3 | 172.19.221.3
IT | F0/4 | 172.19.222.3
Server | F0/5 | 172.19.198.3
Trunk Switch

## Slide 18: Configuration of Access Ports

## Slide 19: Trunk Port
A trunk port can carry traffic for multiple VLANs at the same time
It uses 802.1Q encapsulation to differentiate packets between the VLANs and ensure proper routing and forwarding of data.
This way, the router can handle traffic from different VLANs and enable communication between the VLANs

## Slide 20: Trunk Port Configuration
To ensure the router can be accessed by all VLANs and allows communication between them, the port connected to the router (G0/1) should be configured in trunk mode.
This can be achieved by using the command "switchport mode trunk" on the switch.

## Slide 21: PCs Settings
Departments | Network Address | IP Range | Default Gateway | DNS Server
Finance | 172.19.219.0/24 | 172.19.219.11 – 172.19.219.20 | 172.19.219.1 | 172.19.198.11
Registry | 172.19.220.0/24 | 172.19.220.11 – 172.19.220.20 | 172.19.220.1 | 
HR | 172.19.221.0/24 | 172.19.221.11 – 172.19.221.20 | 172.19.221.1 | 
IT | 172.19.222.0/24 | 172.19.222.11 – 172.19.222.20 | 172.19.222.1 | 

## Slide 22: SERVER

## Slide 23: WEB SERVER

## Slide 25: DNS SERVICE

## Slide 27: FTP SERVER

## Slide 28: FTP SERVER

## Slide 30: Thank You 